## Slide 1: DoS and DDoS resiliency of NDN/CCN architecture Alexander Afanasyev (UCLA), Ilya Moiseenko (UCLA), Lixia Zhang (UCLA), Ersin Uzun (PARC), Priya Mahadevan (PARC)
(Distributed) Denial of Service (DoS) attacks are significant threats to the current Internet
NDN is fundamentally different than IP
  No push: request needed for Data transmission
  Interest/Data flow balance
    Interest and data follow the same path
    Immediate feedback to routers
    Simple multi-path forwarding
Most current (D)DoS attacks on IP are not applicable to NDN.
  no spoofing or reflector attacks
  not as easy to target a specific host
New NDN-specific attacks?
Why interest could be used for DoS?
  Interests are unsolicited
  Each non-collapsible interest consumes state (distinct PIT entry) in intervening routers
  Interests requesting distinct data cannot be collapsed
  Interests routed towards data producer(s)
Can such attacks be prevented?
Yes
Unlike IP routers, NDN routers maintain rich state information that can be used to detect and react to interest flooding
  don’t accept more than can be served
  try not to accept bad Interests
Investigate resiliency of NDN architecture to Denial-of-Service (DoS) attacks
  applicability of existing IP-based
  effect and potential of NDN-specific attacks
  quantify architectural resiliency to attacks
Investigate DoS detection techniques
  traffic pattern analysis
  time series analysis
  sequential change point detection
Investigate DoS prevention/mitigation techniques
  bandwidth-delay-product (BDP) based interest limits
  dynamic per-face interest limiting
  dynamic per-face per prefix interest limiting
  PIT quotas and “replacement” policies
  pushing “bad” Interests to the edges of the network
In small topologies, prevents attackers from injecting excessive # of interests
Does not work in larger topologies
  No differentiation between good and bad traffic
Theoretically, NDN routers have all the information needed to be able to differentiate good interests from bad ones
  To be effective in DoS, bad interests need to be insuppressible and requesting non-existing content
    bad interests = unsatisfiable
  On the other hand, good interests will likely be satisfied with a content
    good interests = satisfiable
  (bad satisfiable interests currently out of scope)
Keep per incoming interface, per prefix (FIB entry) interest satisfaction statistics in routers
Use the statistics to detect and control bad traffic
Current CCNx code does not currently limit the PIT size, or the # of Pending interests for any interface
  Downstream can send more interests than physically possible to satisfy.
NDN architecture opens
opportunities to set limits
NDN has balanced flow between Interests & Data
  Number of Interests defines upper limit on Data packets
The number of pending Interests to fully utilize a link with data packets is:
Interest processing algorithm
  If (per-prefix/per-face) pending Interest limit is not reached
    accept Interest and create PIT entry
  If limit is reached
    “buffer” Interest in per-outgoing face/prefix queue (within per-incoming face sub-queue)
    set weight for per-incoming face sub-queue proportional to observed interest satisfaction ratio
  when new PIT slot becomes available
    accept and create PIT entry for an Interest from queues based on weighted round robin sampling
Result: works partially
  more fair share of resources
  Not effective at differentiating bad and good traffic (no-cache scenario)
  Setting queue sizes and lifetime can get tricky
  Will most likely improve if supplemented with NACKS (under investigation)
Incorporate “active” PIT management
  Limit # of pending Interests per incoming face
    Periodically for every FIB prefix for all faces announce limit for # of pending Interests proportional to the satisfaction ratio
  Do not over-limit
    The sum of all announced limits is at least equal to the sum of output limits
Result: works with all topologies tested
  Does not require much parameter tweaking
  Response time depends on several parameters
    limit announce period
    statistics averaging and time-decaying factors
  Optimization possible to reduce control overhead
    announce only when limits change
Two major threats
Motivation
Interest flooding attacks
Research directions
Physical (bandwidth) limits
Exploring the solution space
The limit alone is not sufficient
Utilizing the state information
Weighted round-robin on Interest queues
Probabilistic Interest acceptance
Dynamic Interest limit adjustments
Satisfaction rates vs. number of attackers in 32-node tree topology
Content Poisoning:
  Adversary introduces junk or fraudulent content
    Pollutes router caches and consumes bandwidth
    Invalid signatures or valid signatures by invalid producers
  Not easy to implement: cannot unilaterally push content
    there will likely be trust mechanisms to register namespaces, etc.
Interest flooding:
  Adversary injects a large number of spurious interests
    Non-sensical distinct interests: not collapsible by routers
    Consume PIT state in intervening routers as well as bandwidth
    Legitimate CCN traffic suffers…
  Easy to implement
  Current CCNx has no countermeasures
Current primary focus
Simulation-based small experimentations
  ndnSIM modular NDN simulator
    http://ndnsim.net
  different scale topologies
    binary trees (3, 31, 127 nodes)
    10Mbps links
    propagation delays randomized from range 1-10ms
    No caching (worst case scenario)
  simple attacker model
    Sends targeted interests (common prefix) for non-existing content
    up to 25% attacker population
  various mitigation techniques
Emulation-based verification
Large scale simulations for promising mitigation techniques
Interest processing algorithm
  “accept” if the outgoing face is utilized under a threshold
  Otherwise, accept with probability proportional to the satisfaction ratio on this face
  Even if satisfaction ratio is 0: “accept” with a low (“probe”) probability
All “accepted” Interests are still subject to (per-prefix/per-face) pending Interest limit
Result: works in general, but requires tweaking
  Parameter selection is important but may not be easy due to topology variances.
  May result in link under-utilization
  Might perform better with NACKs (more accurate statistics)