## Slide 1: (D)DoS in CCN: Evaluation & Countermeasures
September 12, 2012
Ongoing collaborative work between PARC, UCLA and UCI

## Slide 2: What is DoS attack?
Goal: Prevent legitimate resource usage
  i.e., attack on availability
Resources, e.g.,
  Memory, CPU, Bandwidth, Storage etc.
Distributed DoS (DDoS) attacks are common on today’s Internet

## Slide 3: (D)DoS in CCN: IP vs. CCN
CCN is fundamentally different than IP
  Not push based
    Data transmission must be preceded by a request for that data.
    Most DoS attacks in IP are possible because unsolicited data can be sent anywhere
  Reliable Forwarding Plane
    Interest and data follow the same path (i.e., immediate feedback to routers)
    Easy to secure routing (remains challenging in BGP)
    Better resiliency with multi-path routing
  Most current DoS attacks on IP are not applicable to CCN.
What about new DoS attacks, specific to CCN?

## Slide 4: (D)DoS in CCN: Two Major Threats
Content Poisoning:
  Adversary introduces junk or fraudulent content
    Pollutes router caches and consumes bandwidth
    Invalid signatures or valid signatures by invalid producers
  Not easy to implement: cannot unilaterally push content
    there will likely be trust mechanisms to register namespaces, etc.
Interest flooding:
  Adversary injects a large number of spurious interests
    Non-sensical distinct interests: not collapsible by routers
    Consume PIT state in intervening routers as well as bandwidth
    Legitimate CCN traffic suffers…
  Easy to implement
  Current CCNx has no countermeasures
This talk is focused on interest flooding

## Slide 5: Interest Flooding Attacks
Why interest packets could be used for DoS?
  Interests are unsolicited
  Each non-collapsible interest consumes state (distinct PIT entry) in intervening routers
  Interests requesting distinct data cannot be collapsed
  Interests (usually) routed towards data producer(s)
Can such attacks be prevented?
  Short Answer: Yes
  Unlike IP routers, ccn routers maintain rich state information that can be used to detect and react to interest flooding

## Slide 6: Picture of an (interest flooding) attack

## Slide 7: Exploring the solution space
Simulation-based small experimentations
  ndnSIM modular NDN simulator
    http://ndnsim.net
  different scale topologies
    binary trees (3, 31, 128 nodes)
    10Mbps links
    propagation delays randomized from range 1-10ms
    No caching (worst case scenario)
  simple attacker model
    Sends targeted interests (common prefix) for non-existing content
    up to 50% attacker population
  various mitigation techniques
Emulation-based verification
Large scale simulations for promising mitigation techniques

## Slide 8: Brief intro to ndnSIM

## Slide 9: Respecting physical (bandwidth) limits
Current CCNx code does not limit the PIT size, or the # of Pending interests for any interface
  Downstream can send more interests than physically possible to satisfy.
CCN has balanced flow between Interests & Data
  Number of Interests defines upper limit on Data packets
The number of pending Interests to fully utilize a link with data packets is:

## Slide 10: That limit alone is not sufficient
In small topologies, prevents attackers from injecting excessive # of interests.
As expected, it does not work in big topologies
  No differentiation between good and bad traffic.

## Slide 11: Utilizing the state information in routers
Theoretically, CCN routers have all the information needed to be able to differentiate good interests from bad ones.
  To be effective in DoS, bad interests need to be insuppressible and requesting non-existing content.
  On the other hand, good interests will likely be satisfied with a content
Keep per incoming interface, per prefix (FIB entry) interest satisfaction statistics in routers
Use the statistics to detect and control bad traffic.
Notes: Exponential moving average statistics.

## Slide 12: Weighted round-robin on interest queues
when an Interest arrives
  If (per-prefix/per-face) pending Interest limit is not reached
    accept Interest and create PIT entry
  If limit is reached
    “buffer” Interest in per-outgoing face/prefix queue (within per-incoming face sub-queue)
    set weight for per-incoming face sub-queue proportional to observed interest satisfaction ratio
  when new PIT slot becomes available
    accept and create PIT entry for an Interest from queues based on weighted round robin sampling

## Slide 13: Weighted round-robin results
Partially works
  more fair share of resources
  Not effective at differentiating bad and good traffic (no-cache scenario)
  Setting queue sizes and lifetime can get tricky
  Will most likely improve if supplemented with NACKS (under testing)
Notes: Queue lifetime 100ms, interest lifetime 1 sec.

## Slide 14: Probabilistic Interest acceptance/drops
When an Interest arrives
  “accept” if the outgoing face is utilized under a threshold
  Otherwise, accept with probability proportional to the satisfaction ratio for Interests on this face and per-prefix
  Even if satisfaction ratio is 0: “accept” with a low (“probe”) probability
All “accepted” Interests are still subject to (per-prefix/per-face) pending Interest limit
Notes: Threshold 25% of window size

## Slide 15: Probabilistic Interest acceptance Results
Parameter selection is important but may not be easy due to topology variances.
May result in link under-utilization
Works in general,
Might perform better with NACKs (more accurate statistics)

## Slide 16: Dynamic Interest limit adjustments
Incorporate “active” PIT management
  Periodically
    for every FIB prefix
      for all faces
        Announce NoPI limit proportional to the satisfaction ratio
  Min limit is 1 and sum of all announced limits is at least equal to sum of output limits
Notes: In simulations, period is set to 1 sec.

## Slide 17: Illustration of Dynamic limits
50
50
50
50
50
50
50
50
1.0
1.0
1.0
1.0
1.0
NA
NA
1.0
Just before the attack
Satisfaction rates
Announced limits
50
50
25
25
25
25
25
25
1.0
1.0
0.5
0.5
1.0
0.0
0.0
1.0
Immediately after attack starts
Satisfaction rates
Announced limits
50
50
45
45
25
1
1
25
1.0
1.0
0.9
0.9
1.0
0.0
0.0
1.0
Stabilized after the attack
Satisfaction rates
Announced limits

## Slide 18: Dynamic limits results
Does not require much parameter tweaking
Works with all topologies tested

## Slide 19: Large scale experimental setup
Rocketfuel Sprint topology
7337 routers and 10 000 links
Only adjacency = no link characteristics info
Extract
  535 backbone routers
  3339 gateway routers
  3463 customer routers
Backbone <-> Backbone links are 100Mb with 70ms delay
Backbone <-> Gateways links are 10Mb with 20ms delay
Gateway <-> Customer links are 1Mb with 20ms delay

## Slide 20: Large scale results

## Slide 21: Thanks!
Questions?

## Slide 22: BACKUP SLIDES

## Slide 23: Overall evaluation results
Four-level tree
Different number of attacker nodes
  1-8 attackers (6%-50%)
Different DDoS mitigation algorithms
  dynamic Interest limit adjustments
  probabilistic Interest accept
  Queues with weighted round robin
  PIT limits respecting physical link bandwidth (bandwidth-delay product)
  no limits

## Slide 24: Interest satisfaction ratios
10-run averages

## Slide 25: Reaction to the attack (satisfaction vs. time)
4 (25%) attackers
Notes: 95% confidence intervals

## Slide 26: Emulation vs. Simulation
Simulation is the primary evaluation tool in this project
NDN simulator vs CCNx ?
In Deterlab emulate CCNx in DDoS scenario on a small tree topology
Simulate the same in NDN simulator
Notes: In emulation we have a real operating system Linux Ubuntu 10 with CCNx 0.6.0 installed
In emulation we have Java applications that use a normal java CCNx API and have the same functionality as applications in ndnSIM (Producer app, consumer app, malicious app)
Setup is as on the picture with 100Kb links, 40ms delay
Evil apps send packets every 2ms in emulation and every 2.8ms in simulation
Consumers send interests every 200ms
Producer is installed on the root node
All clients are on the leaves

## Slide 27: Results of comparison
Shows the strength of DDoS attack (adjusted)
Malicious app sends Interests every 2.8 ms in simulation & 2ms in emulation (Operating System scheduling effect)
Shows successful data retrieval by legitimate consumers
DDos attack on [60,90] seconds
Notes: Overall Simulation and Emulation provide a similar results after making a reasonable adjustments.
ndnSIM performs worse due to its deterministic nature, while the effects of UDP protocol usage, operating system scheduling, and kernel level operations on packet queues provide more randomness and a better intermixing of bad and good traffic that give a better perofrmance.

## Slide 28: Large scale experimental setup
Realistic Internet scale topology
Rocketfuel Sprint topology (and others in future e.g. ATT)
Sprint is 7337 routers and 10 000 links
Only adjacency = no link characteristics info
Extract
  535 backbone routers
  3339 gateway routers
  3463 customer routers
Backbone <-> Backbone links are 100Mb with 70ms delay
Backbone <-> Gateways links are 10Mb with 20ms delay
Gateway <-> Customer links are 1Mb with 20ms delay

## Slide 29: Large scale experimental setup
Randomly choose 1 backbone router and install Producer app
Randomly choose 1%, 5%, 10%, 25% and 50% of customer routers that will have a malicious app installed on them
All other customer routers have a legitimate app installed

## Slide 30: Large scale results

## Slide 31: Large scale results

## Slide 32: Probabilistic model. Effect of bad params
Performance may suffer significantly if parameters of the probabilistic model are adjusted incorrectly
  “grace” acceptance increased from 1% to 5% compared to previous slide

## Slide 33: Results on UCI’s pushback mechanism (poseidon)

## Slide 34: PUSH-BACK OVER COMPLEX TOPOLOGIES
Deutsches ForschungsNetz

## Slide 35: PUSH-BACK

## Slide 36: PUSH-BACK
Baseline content traffic (no attack)
Content traffic under attack
With push-back-based countermeasure